## Slide 1
CIJE · GETTING STARTED
From Box to Branch
Setting up your CIJE Birdwatcher, from unboxing to your first AI-powered sighting
Self-paced · about 60 minutes · DFR1154 ESP32-S3

## Slide 2
THE HARDWARE
What's inside your Birdwatcher
One small board carries everything: eyes, ears, a voice, and a line to OpenAI.
ON THE BOARD
Hardware
ESP32-S3R8
Dual-core 240MHz + 8MB PSRAM
OV3660 Camera
160° wide-angle, infrared capable
PDM Microphone
Built-in I2S digital mic
MAX98357 Amp
I2S speaker output for TTS audio
SD Card Slot
Expandable media storage
16MB Flash
Ample firmware + asset storage
IN THE CLOUD
AI capabilities
GPT-4 Vision
Identifies birds & analyzes images
Whisper STT
Speech-to-text from the mic
TTS Playback
OpenAI text-to-speech via speaker
Live Streaming
Real-time camera feed in browser
Gallery Manager
Timestamped SD card file system
Export Packages
Download analysis + media bundles
Under the hood: a $35 board plus OpenAI's cloud. A complete AI birdwatcher in the palm of your hand.

## Slide 3
THE BOARD
Every port and sensor, at a glance
OV3660 Camera
160° wide-angle lens, IR capable
PDM Microphone
GPIO 38/39, I2S interface
MAX98357A Speaker
I2S amplifier, GPIO 45/46/42
IR Illumination
GPIO 47, for low-light imaging
ALS Sensor
LTR-308 ambient light, GPIO 8/9
SD Card Slot
Up to 16GB, SPI interface
Type-C USB
Power input + code upload port
Gravity Connector
GPIO 43 (TX) / 44 (RX) for Arduino
One USB-C cable does it all: power, firmware upload, and the serial monitor.

## Slide 4
BEFORE YOU START
What you need
REQUIRED HARDWARE
DFR1154 module (your Birdwatcher)
USB-A to USB-C data cable
Laptop (Windows, Mac, or Linux)
WiFi network with internet access
Optional: AI Camera tripod kit
Optional: small speaker (MX1.25-2P)
SOFTWARE SETUP
Arduino IDE 2.x (free download)
ESP32 board package by Espressif
ArduinoJson library v7.4.2+
Board: ESP32S3 Dev Module
USB CDC On Boot: Enabled
PSRAM: OPI PSRAM
ACCOUNTS & KEYS
OpenAI account (platform.openai.com)
Personal OpenAI API key (sk-...)
API credits (a few dollars is plenty)
WiFi SSID + password (home or school)
GitHub account (optional)
SD card 8–32GB, FAT32 formatted
Estimated cost: board ~$35 | analysis ~$0.05–0.10 per request | Arduino IDE free

## Slide 5
REFERENCE
GPIO pin cheat sheet
Bookmark this page. You will not need it during setup, but it earns its keep the day you start extending the firmware.
CAMERA (OV3660)
XCLK
5
Y9
4
Y8
6
Y7
7
Y6
14
VSYNC
1
HREF
2
PCLK
15
SIOD
8
SIOC
9
MIC (PDM)
CLK
38
DATA
39
SPEAKER
BCLK
45
LRCLK
46
DIN
42
GAIN
41
MODE
40
SD CARD
MO
11
MI
13
SCLK
12
CS
10
OTHER
LED
3
IR
47
BOOT
0
TX
43
RX
44
Camera and audio share I2S_NUM_0, so they cannot run at the same time. Recording briefly pauses the stream. That is by design.

## Slide 6
STEP 01 · ARDUINO IDE
Point Arduino at the ESP32
1
Three one-time setup moves in Arduino IDE 2.x. You will never repeat these.
A. BOARD MANAGER
1
Open File > Preferences
2
Add to Additional Boards Manager URLs:
raw.githubusercontent.com/espressif/
arduino-esp32/gh-pages/package_esp32_index.json
3
Tools > Boards Manager: install esp32 by Espressif Systems
B. BOARD SETTINGS (TOOLS MENU)
Board
ESP32S3 Dev Module
USB CDC On Boot
Enabled
Flash Size
16MB (128Mb)
Partition
16M (3MB APP/9.9MB FATFS)
PSRAM
OPI PSRAM
C. LIBRARY
ArduinoJson
by Benoit Blanchon
v7.4.2 or newer
Sketch > Include Library > Manage Libraries
Install timing out? Add connection_timeout: 600s under network: in arduino-cli.yaml, restart the IDE, and retry.

## Slide 7
STEP 02 · GET THE CODE
Download the firmware from GitHub
2
THE REPO
oyyeahhh / birdwatch-cam
1
Open github.com/oyyeahhh/birdwatch-cam
2
Navigate to ai_camera/firmware/standalone
3
Download ai_camera_3.2.0.zip
4
Unzip and keep the .ino together with all three .h files in one folder
While you are there: can you find the CAD files for the tripod?
WHAT YOU SHOULD SEE
ESP32_AI_Camera_v3_2_0.ino
credentials_manager.h · error_handling.h · ssl_validation.h
Prefer a no-code path? The repo's ai_camera/GETTING_STARTED.md walks through a browser-based flasher. No Arduino IDE needed.

## Slide 8
STEP 03 · CREDENTIALS
Tell it your WiFi, and hand it the key
3
ESP32_AI_Camera_v3_2_0.ino · around lines 46–48
const char* ssid = "YourWiFiSSID";
const char* password = "YourWiFiPassword";
const char* OPENAI_API_KEY = "sk-proj-xxxxxxxxxxxx";
// Save > Verify (✓) > Upload (→)
Replace all three placeholder values with your own, then save.
GOOD TO KNOW
Your network
Use your own WiFi
The camera and your browser must be on the same network.
2.4 GHz works best
The ESP32 does not join 5 GHz-only networks.
Never commit real credentials to GitHub. The repo's secrets_template.h pattern exists exactly so keys stay out of your commits.

## Slide 9
STEP 03 · THE KEY
Get your OpenAI API key
3
This is what lets your Birdwatcher talk to GPT-4 Vision. It takes about three minutes.
1
Sign in at platform.openai.com (create an account if needed)
2
Open the API Keys page and click “Create new secret key”. Name it Birdwatcher.
3
Copy the key (it starts with sk-...) and store it somewhere safe. You cannot view it again.
4
Paste it into the OPENAI_API_KEY line from the previous page.
COSTS
Pennies, not dollars
Each analysis costs roughly $0.05–0.10.
Set a monthly cap
Settings > Limits in the OpenAI dashboard, so there are no surprises.
Your key is personal. Treat it like a password: never share it, and never paste it into a public repo.

## Slide 10
STEP 04 · UPLOAD
Upload the firmware, watch it boot
4
1
Connect the board via USB-A to USB-C
2
Tools > Port: select your camera's COM port
3
Click Upload (the → arrow)
4
Wait ~2–3 minutes for compile + upload
5
Open Serial Monitor at 115200 baud
6
Watch for the IP address in the output
SERIAL MONITOR
====================================
ESP32-S3 OpenAI Interface v3.2.0
====================================
SD Card OK
Camera OK
PDM Microphone OK
Speaker OK
Connecting to WiFi...
WiFi connected
IP: 192.168.0.181
See the IP? Open a browser on the same WiFi and type it in, e.g. http://192.168.0.181 — that page is your Birdwatcher.

## Slide 11
CHECKPOINT
Your setup checklist
Steps 1–4 in one place. Tick each box on your way through.
TASK A · HARDWARE
1
Unbox the DFR1154 camera module
2
Attach tripod bracket (if using)
3
Connect USB-A to USB-C to laptop
4
Board powers on (LED lights)
5
Open Arduino IDE
TASK B · IDE & FIRMWARE
1
ESP32 board package installed
2
Board: ESP32S3 Dev Module
3
Apply the 5 settings from Step 1
4
Open ESP32_AI_Camera_v3_2_0.ino
5
Enter WiFi SSID, password, API key
TASK C · UPLOAD & CONNECT
1
Select the right COM port
2
Click Upload (→)
3
“Done uploading” appears
4
Serial Monitor at 115200 baud
5
Note the IP address shown
Success looks like: the Birdwatcher web interface loading at your camera's IP address.

## Slide 12
THE INTERFACE
The web app, left to right
No app to install. Everything lives on one page served by the camera itself.
LEFT PANEL
Camera & controls
Pairing Workflow Banner
Yellow bar shows your current step
Start / Stop Stream
Toggles the live camera feed
Capture
Takes a still photo, saves to SD card
Review
Previews the most recent capture
LIVE Indicator
Green dot: stream is broadcasting
Camera Preview
Live MJPEG from the wide-angle lens
RIGHT PANEL
Audio & files
Audio Playback Bar
Plays back recorded WAV files
Record
Starts/stops the PDM mic recording
Speaker
Controls TTS playback volume
Image for Export
The photo you will send to OpenAI
Audio for Export
Your spoken prompt for Whisper
Resources
All SD files: save to PC, export, delete
Browser says “Not Secure”? Expected. The camera uses a self-signed certificate on your local network.

## Slide 13
THE INTERFACE
Where the AI answers
Send to OpenAI
Ships your image + spoken prompt to GPT-4 Vision and Whisper. The reply is displayed, then spoken aloud.
Replay TTS
Re-plays the last spoken response through the speaker, without calling the API again.
Export Package
Downloads a ZIP with the image, your audio prompt, and the AI's response text.
THE RESULTS BOX
The large text area under the video shows the GPT-4 Vision response, speaks it through the speaker, and archives it to the SD card in /analysis/[timestamp]/.
A real reply: “That is a Northern Cardinal, a male based on the bright red plumage, perched on the feeder's left arm...”

## Slide 14
THE WORKFLOW
The loop you'll run every session
1
START
STREAM
Live feed begins
2
CAPTURE
IMAGE
Frame it, save to SD
3
RECORD
PROMPT
Speak your question
4
ADD TO
EXPORT
Pick image + audio
5
SEND TO
OPENAI
Answer is spoken
AFTER THE ANALYSIS
Replay TTS
Export package
Delete files
Reset & repeat
Stream, capture, ask, send. After a couple of rounds the whole loop takes under a minute.

## Slide 15
TROUBLESHOOTING
When something squawks
Board not found / no COM port
Install the CH340 or CP2102 USB driver. Swap in a data cable (many are charge-only). Hold BOOT while plugging in.
Upload fails: brownout / timeout
Set Flash Size 16MB and the 16M partition scheme in Tools. Try a powered USB hub.
Camera stream not showing
Enable USB CDC On Boot, then refresh the browser. Recording audio pauses the stream briefly.
OpenAI returns 401 / 403
Check the key has no extra spaces and billing is enabled at platform.openai.com.
TTS / speaker silent
Check the SPK connector wiring (MX1.25-2P). The amp uses GPIO 45 / 46 / 42.
SD card not detected
Reformat as FAT32, use a 16GB-or-smaller card, and re-seat it before power-up.
Still stuck? wiki.dfrobot.com/SKU_DFR1154 has the full hardware reference for the board.

## Slide 16
FAQ
Quick answers
Q: Is the “Not Secure” warning a problem?
No. The firmware keeps traffic encrypted but uses a self-signed certificate, which browsers flag on local networks.
Q: Why does the page freeze during analysis?
The ESP32 is single-threaded. It pauses 15–30 seconds while talking to OpenAI. Normal.
Q: Why can't I record while streaming?
Camera and mic share one I2S bus. Recording briefly takes it over, then the stream resumes.
Q: How big can the SD card be?
FAT32, 32GB max. 8–16GB is the sweet spot.
Q: Does the mic sound quiet?
Audio gets 10x software amplification. Speak within a few feet of the board.
Q: Can it drive other hardware?
Yes. The Gravity connector (TX 43 / RX 44) speaks serial to an Arduino UNO. See the automation agent firmware.
Most “bugs” are design choices of a tiny computer doing big things. The Known Limitations section of the repo README explains each one.

## Slide 17
WHAT'S NEXT
Make it yours
YOUR NEXT STEPS
1
Mount your Birdwatcher near a feeder or window
2
Keep a log of the species your camera spots
3
Try the Automation Agent firmware next
4
Design ONE lesson that integrates AI vision
5
Share what you built with your department or PLN
6
Explore the repo, then fork it and make it yours
KEEP EXPLORING
Birdwatcher repo
github.com/oyyeahhh/birdwatch-cam
DFRobot wiki
wiki.dfrobot.com/SKU_DFR1154
OpenAI platform
platform.openai.com
Arduino IDE
arduino.cc/en/software
ESP32 tutorials
randomnerdtutorials.com
AI4K12 framework
ai4k12.org
Every fork keeps this project alive. When you extend the Birdwatcher, you become part of the lineage that started with BirdNET.

## Slide 18
Happy birdwatching.
Questions? The CIJE Innovation team is a message away.
github.com/oyyeahhh/birdwatch-cam